## Slide 1: Cryogenic Distribution
Tom Peterson, SLAC
USPAS
January, 2017

## Slide 2: Cryogenic distribution
This portion of the class will focus on certain topics in the design and fabrication of distribution equipment for large cryogenic systems
  Transfer lines
  Feed and distribution boxes

## Slide 3: Distribution function
These devices serve as the interface from a cryogenic plant to specialized cryogenic equipment.
Such cryogenic "boxes" may include
  Thermal transitions of various kinds
  Power leads for electric current
  Instrumentation
  Vacuum barriers
  Control valves, relief valves, etc.

## Slide 4: Outline Cryogenic distribution
Transfer lines
Vacuum barriers
Lambda plugs
Feed and distribution boxes
LCLS-II distribution system overview

## Slide 5: Cryogenic transfer lines
Techniques have become fairly standard
Stainless vacuum pipe
Stainless (or sometimes copper) inner lines
Plastic or composite material (e.g., G-11 epoxy-fiberglass) supports

## Slide 6: Fermilab’s 4.5 K transfer line
Supplies 4.5 K, supercritical (3 bar) helium over 6 km to “satellite” refrigerators
Also provides LN2
Inner pipe (4.5 K helium)
Insulating vacuum space
Liquid nitrogen space
Insulating vacuum space

## Slide 7: Fermilab’s 4.5 K transfer line
Outside on top of the accelerator enclosure, a full 6 km circumference ring
Here a bypass around a building

## Slide 8: Common transfer line issues
Long lengths mean many welds
  Leak checking may be a challenge
  Division of insulating vacuum into manageable sections
Thermal contraction allowance
  Bellows and flexible hose, quality control issues
  Different lines may shrink or expand first
Inner line supports
  Wear or bind with frequent thermal cycles
  May involve use of plastics, requiring use of proper materials to avoid brittle failures

## Slide 9: DESY TTF transfer line - 1
4.5 K and thermal shield flow from HERA cryo-plants to TTF

## Slide 10: DESY TTF transfer line - 2
4.5 K and thermal shield flow from HERA cryo-plants to TTF

## Slide 11: DESY TTF transfer line - 3
Entrance to TTF building (Hall 3)

## Slide 12: DESY TTF transfer line - 4
Distribution box at TTF end of transfer line

## Slide 13
From Vittorio Parma (CERN) -- Provides nice comparison of
cryostat and transfer line structures

## Slide 14: CERN QRL installation

## Slide 15: Reported transfer line heat loads
Tevatron (C. Rode, et. al., in Advances in Cryogenic Engineering, Vol 27, pg. 769)
  80 K to 4.5 K ~33 mW/m (48 mm OD)
  300 K to 80 K ~0.5 W/m
HERA (M. Clausen, et. al., in Advances in Cryogenic Engineering, Vol 37A, pg. 653)
  40-80 K to 4.5 K ~130 mW/m (60 mm supply + 140 mm return), consistent with about 210 mW/m2 of inner line (compare to 50 mW/m2 for heat load through MLI)
  300 K to 40-80K ~1.0 W/m
LEP flexible transfer lines (H. Blessing, et. al., in Advances in Cryogenic Engineering, Vol 35B, pg. 909.
  30 mW/m on inner (4.5 K) line (13 mm OD)

## Slide 16: Some reported transfer line costs
CERN and Fermilab estimate from recent experience
  ~$8000/meter for large (600 mm OD vac jacket) transfer line (installed cost)
Fermilab estimate
  ~$1000/meter for typical, small 4.5 K transfer line (installed cost)

## Slide 17: Vacuum barriers
Separate insulating vacuum into manageable sections
  Leak checking and trouble-shooting
  Reduce extent of accidental loss of vacuum
  Regions for vacuum instrumentation

## Slide 18: Vacuum barrier schematic

## Slide 19: CERN’s Short Straight Section Vittorio Parma -- CERN

## Slide 20: Vacuum barrier in SSS

## Slide 21: Lambda plugs
An end box for pressurized superfluid will need to pass instrumentation and power into the superfluid region
  Feedthrough via vacuum space, directly to SF volume
    Risk of helium to vacuum leak
  Feedthrough via 4.5 K helium space to superfluid space
    Must limit heat transfer from 4.5 K to 2 K
    This is sometimes called a “lambda plug”
    Typically required for current leads
    LHC has many
Failure results in a heat load to 2 K level

## Slide 22: Simplified LHC magnet cooling scheme
Lambda plug
4.5 K
2 K

## Slide 23: Lambda plug fabrication (LBNL)- 1
Superconducting cable potted in an insulating block of G10-CR
  Plane of reinforcement parallel to faces
  Four 8 kA cables and 24 200-600 A cables
Plug design and procedures developed at Berkeley Lab

## Slide 24: Lambda plug fabrication - 2
Encapsulated in Stycast 2850MT (blue) epoxy using hardener 24LV
Application via injection in a vacuum chamber

## Slide 25: Lambda plug installed -1 View of lambda plug from 4.5 K helium vessel

## Slide 26: Lambda plug installed -2 View of lambda plug installation from vacuum space

## Slide 27: Lambda plug installed -3 View of support flange and 1.9 K pipe from insulating vacuum space

## Slide 28: Allowable leak rate -- example
For these lambda plugs, an allowable leak rate was determined based on allowable heat transport through a crack
  0.15 mm channel results in less than 1 mW heat from 4.5 K side to 1.9 K side
Channel size converted to an equivalent room temperature air flow
Air leak rate measured as a QC check

## Slide 29
From Tc = 1.9 K to T-lambda, W = 4.8
For L = 5 cm, heat flux q = 3.0 W/sq.cm.
For a 0.15 mm diameter channel, the
heat transferred is less than 1 mW

## Slide 30: TTF feed box
TESLA Test Facility (TTF) at DESY is a small SRF system, so feed box is like an SRF test feed box
  Receives 4.5 K He
  Internal heat exchangers for 2 K generation
  Connection to large room temperature pump
Designed and built at Fermilab for TTF at DESY

## Slide 31: TTF feedbox schematic
Photo of this on the next page

## Slide 32: TTF feedbox internal
2 K end of piping
  4.5 K to 2 K heat exchanger
  Large vent line
Note short braided hose on large vent pipe for small thermal motion
Copper thermal shield
Heat exch
Large vent
pipe

## Slide 33: LHC test string 2 feed box (CERN)
Many current leads and ports for access to make splice joints

## Slide 34: Distribution box: DFBX
Distribution feed boxes (DFBX) for LHC at CERN
Designed by Lawrence Berkeley National Lab with assistance from Fermilab
Provide cryogens, electrical power, and instrumentation interface between CERN cryogenic system and US-supplied final focus quadrupoles

## Slide 35: LHC magnet cooling scheme

## Slide 38: LCLS-II Cryogenic Distribution

## Slide 39: LCLS-II Feed Caps 2 and 4 (Arkadiy Klebaner, Fermilab, and DEMACO)

## Slide 40: LCLS-II BC1 Bypass (Arkadiy Klebaner, Fermilab, and DEMACO)

## Slide 41
Conclusion:
Cryogenic distribution equipment
often occupies a major fraction
of cryogenic engineering time
for a project. It may be non-
standard, integrates many
different components into one
cryostat, and involves sizing of
valves, relief valves, pipes,
pressure vessel issues, heat
transfer considerations, etc., etc.
Significant and interesting
mechanical engineering!

## Slide 42: References
V. Parma, “Construction Experience of the LHC Cryostats,” presentation at ILC GDE meeting, 11 Sep 2007
C. Rode, et. al., “Fermilab Tevatron Transfer Line,” in Advances in Cryogenic Engineering, Vol 27, pg. 769.
M. Clausen, et. al., “Cryogenic Test and Operation of the Superconducting Magnet System in the HERA Proton Storage Ring,” in Advances in Cryogenic Engineering, Vol 37A, pg. 653.
H. Blessing, et. al., “Very Low-Loss Liquid Helium Transfer with Long Flexible Cryogenic Lines,” in Advances in Cryogenic Engineering, Vol 35B, pg. 909.